## Slide 1: Module 4: Analog programming blocks

## Slide 2: Module Objectives
Analyze a control task that uses analog inputs.
Connect a potentiometer to LOGO! controller and use it for simple control tasks.
Configure control task hardware by calculating the required resistance for a given potentiometer’s specifications.
Adjust the ON/OFF delay timers’ parameters using a potentiometer.
Use Analog comparator and analog amplifier programming blocks.

## Slide 3: Analog and Digital signals
A signal is any type of physical quantity that conveys information.
Electrical signals can be classified into analog signals and digital signals.
An analog signal is a kind of signal that varies continuously, While a digital signal has discrete levels.

## Slide 4: Examples
When you talk to any one you use Audio signal.
To turn a light ON you need to send an electrical signal.
This text is another kind of signal.
Analog signals
Digital signals

## Slide 5
Consider a light switch that is either ON or OFF, this light switch is an example of a digital input device
Think about a dimmer switch that allows you to vary the light in different degrees of brightness. In this case the switch has potentiometer that can be used as an analog input.
Digital inputs are used to control digital signals while analog inputs are used to control analog signals.
Many signals in our daily life are analog signals, for example, voice, audio, video, temperature, pressure, or position

## Slide 6: Processing analog quantities
The LOGO! 12/24RC is equipped with the inputs I7 and I8, which can also be programmed as analog inputs (AI1 and AI2).
LOGO! can read voltages from 0 to 10 V or currents from 0 to 20 mA at its analog inputs.
Therefore, the physical quantities (e.g. temperature, pressure, speed etc.) must be converted into electrical quantities.
This conversion is performed by an external sensor.

## Slide 7: The steps required to process analog inputs.

## Slide 8
In figure,a sensor is connected to the analog input of LOGO!. It converts a physical quantity into an electrical signal.
This value of signal lies within the typical range of this sensor.
LOGO! reads an electrical quantity at the input and convert it into a standardized value within the range of 0 to 1000.
This value is then processed by the special analog functions used in the program.
Based on the program conditions, LOGO! then switches ON or OFF an external actuator.

## Slide 9: Connecting potentiometer to LOGO!
For LOGO! Controller the input voltage range is 0-10V.
When connecting any analog input this range must be taken into consideration.
To get a 10V maximum reading with a full rotation of the potentiometer (depending on the potentiometer input voltage), sometimes you have to connect another series resistor.

## Slide 10
if there is an input voltage of 24 V and you want to use a potentiometer to give a 10V input voltage as a maximum value, then the difference in voltage can be achieved by connecting a resistor in series with the potentiometer such that a maximum 10V value is obtained with a full rotation of the potentiometer.

## Slide 11
The following formula can be used to obtain the value of the required resistor:

## Slide 12
A 20KΩ potentiometer is to be used as an analog input for a LOGO! Controller, if the supply voltage is 24V, find the value of the resistor that should be connected in series with this potentiometer.

## Slide 13: Analog threshold trigger
The output of this programming block is set or reset depending on two configurable thresholds; one is ON threshold the other is OFF threshold.

## Slide 14: Functional description
This function fetches the analog signal atinput Ax .
Ax is multiplied by the value of the A ( gain ) parameter,and the value at the parameter B (OFFSET) is added to the product
i.e (Ax . Gain ) + offset = actual value of Ax

## Slide 15
Calculation rule
If threshold (On) >= threshold (Off), then:
Q = 1, if the actual value Ax > On.
Q = 0, if the actual value Ax <= Off.
If threshold (On) < threshold (Off), then:
Q = 1, if On <= the actual value Ax < Off

## Slide 16: Timing Diagram

## Slide 17: Air Conditioning machine
The function block diagram can be used to switch ON an Air Conditioning machine when the temperature is more than 23 and OFF when the temperature is less than 19, this will maintain the room at an optimum temperature and will save energy too.

## Slide 18: Using potentiometer as parameter for timer and counter
It is possible and very useful to control a parameter for timer or counter using a potentiometer.
The analog input values of the potentiometer can be captured from an analog input. The timer value of an on/off delay or the switch on/off limit off a counter can be linked to the analog value

## Slide 19: Steps involved
Open the Properties dialog of the counter or timer element.
Via the "Reference" button specify the analog value to be used as parameter.

## Slide 20: Analog comparator
Analog comparator is used to compare between two analog signals.
The output of this programming block is set and reset depending on the difference between those two signals (Ax – Ay) and on two configurable thresholds (ON-threshold and OFF-threshold).

## Slide 21: Symbol

## Slide 22: Analog amplifier
Analog amplifier is used to amplify an analog input signal
The output of this programming block is an amplified version of the input signal.

## Slide 23: SYMBOL